## Slide 1: Explorer Post 3.14
autoAuto Project
– 2014 Intro

## Slide 2: AROBOTS Project – completed concept
Software Modules

## Slide 3: AROBOTS Project – motion path concept
Can you end at the SAME place you started?
START

## Slide 4: autoAuto – autonomous track-following ground vehicle - Project
Concept
  Ground Vehicle includes master control computer and sensor suite
  Line sensors detect ground track, provide guidance error information
  Obstacle sensor detects obstacle to avoid collision
  Ground Vehicle autonomously:
    Waits for user command to start
    Finds ground track, follows ground track
    Detects obstacles before collision and stops
    Finds end of track and stops

## Slide 5: Activities – Mechanical Engineering Vehicle Group
Starting Point – Old RC vehicle
  Engineering analysis – vehicle will not support requirements
Starting Point – Select robotics development vehicle
  Started with a pile of parts
Mechanical Engineering Tasks
  Characterize motor controller
  Design drive train, motors, controller use
  Assemble vehicle
  Wire drive motors and controllers
  Mount controller board
  Troubleshoot motor operation
  Redesign power supply
  Mount, wire, and integrate sensors
  Mount, wire, and integrate display(s)

## Slide 6: Activities – Electrical Engineering Sensor Group
Starting Point – Select candidate sensor technologies
  Range sensor
  Line sensor
Electrical Engineering Tasks
  Characterize ultrasonic range sensor
    Detection ranges
    Input signals, output signals
    Power requirements
  Characterize infrared range sensor
    Detection ranges
    Input signals, output signals
    Power requirements
  Characterize line sensor
    Detection ranges
    Line and background requirements
    Input signals, output signals
    Power requirements
  Suggest mounting requirements

## Slide 7: Activities – Software Engineering Software Group
Starting Point – Select arduino uno microcontroller
    Engineering analysis – microcontroller will not support requirements
Software Engineering Tasks
  Specify more powerful arduino mega microcontroller
  Develop top-level software design
  Develop detailed software components
  Integrate software components
  Develop software to support vehicle characterization and integration
  Develop software to support system testing
Team Activities
  Individuals bring personal laptops to support parallel team efforts
  Cross training between team members
  Creation of central repository on GitHub

## Slide 8: Lessons Learned
Engineering Process
  Follow Engineering Process to work through challenging “unknowns”
Documentation
  Create and maintain engineering notebooks for each working group
Team Work
  Support parallel software development by allowing personal computers
  Embed subject matter experts into other working groups
Requirements and Specifications
  Initial requirements were incomplete and not well understood
  Stand up System Engineering Working Group
Group Dynamics
  People come and People go
    need to support new members AND maintain progress of project
  autoAuto took too long to perform
    Improve how we schedule work
    Select projects with shorter timelines
    Develop interim project phases to increase challenge and fun

## Slide 9: Activities – System Engineering Group
Starting Point – Assumed system engineering by management activity
    Management did not perform system engineering
    Working groups drifted, activities not efficient
System Engineering Tasks
  Took ownership of system requirements
  Led Technical Requirements Review (TRR) with customer
    Discussed customer view of system requirements and typical integration issues
    Discussed customer view of desirable use of technology
  Conducted requirements analysis
    Based on initial concept
    Filled in requirements to make consistent and complete
  Assign requirements responsibility to working groups
  Design test requirements
  Assign test requirements to test plan
  Develop test range
  Execute testing to verify requirements compliance
  Study project management concepts

## Slide 10: Working on autoAuto
Select a working group (or try them all)
Contribute your expertise and ideas
Learn from your colleagues and advisors
Keep notes and ask questions
Have Fun!
Top Level Schedule
  October
    Complete assembling vehicle, debugging as required
    Complete development of software modules, begin integration
    Complete system requirements assignments
    Complete test requirements and test schedule
    Begin developing test range
  November
    Complete system integration, debug as necessary
    Begin testing, debug and retest as necessary
  December
    Complete testing. Declare system meets requirements. Deliver to customer.

## Slide 11
BACKUP

## Slide 12: Project Update
Concerns related to the ability to adequately control the speed and turning of the Hummer vehicle (used on the previous project) prompted us to find another vehicle
  Speed appears to be either go full or stop – no intermediate speeds
  Turns appear to be either full left or full right – no small turns
Purchased 2 identical vehicle kits:
  4WD Mobile Platform
  Motor controller & encoders
  Microcomputer board
  Ultrasonic obstacle sensor
  Distance sensor
  Bluetooth
  Cables
  Etc.
Purchased a line-detector sensor recommended by a Dynetics robotics expert
Vehicle platform and sensors can be used on future projects

## Slide 13: Inventory of Components Purchased
Digital Sensor Cable For Arduino (10 Pack) FIT0011
LCD Keypad Shield For Arduino DFR0009
Analog Sensor Cable For Arduino (10 Pack) FIT0031
USB Cable A-B for Arduino FIT0056
Baron-4WD Mobile Platform ROB0025
2A Dual Motor Controller DRI0002
DFRobot Bluetooth V3 TEL0026
Bluetooth Adapter Mini TEL0002
Sharp GP2Y0A21 Distance Sensor (10-80cm) SEN0014
Line Tracking Sensor for Arduino SEN0017
DFRobot mega2560 V2.0 (Arduino mega 2560 R2 compatible) DFR0191

## Slide 14: Vehicle
Voltage: +4.5 to 6V
Current: 1200mA load
Motor type: 130
Rotational Speed: 10000 r / min
Gearbox reduction ratio: 1:120
Maximum speed: 68cm / s
Wheel diameter: 65mm
Dimensions: Length 230mm Width 185mm high 110mm
Weight: 614 grams (without batteries)
Maximum load: 800g

## Slide 15: autoAuto Project Teams
Project has 4 key development areas to address:
  Control of vehicle speed and steering
  Line-follow detection
  Obstacle detection
  Vehicle controller software executive program
Establish 4 teams to individually focus on a key development area
  All 4 key development areas will be simultaneously addressed
  Any problem areas will be quickly identified, discussed, & a path forward developed
  Individuals will gain experience with subsystem/system integration
  Individuals will have exposure to multiple technical domains:
    Requirements & Specifications Development & Requirements Management
    System Integration & Interface Management
    Mechanical Design
    Electrical Design
    Guidance and Control
    Software Development
    Subsystem & System Test

## Slide 16: Team 1- Motor & Steering Control Subsystem
Assemble and inspect vehicles to understand motor and motor driver/encoder characteristics
Review information and vehicle to understand motor connections, encoder operation/output, motor control, and perhaps characterize encoder
  Encoder output (pulse rate related to motor speed? Ex: no. of pulses per motor shaft revolution)
  Define control/electrical interface of motor and encoder
Develop algorithm to proportionally control motor speed
  Use encoder feedback to control motor speed?
  Develop performance specification
  Develop algorithm interface description
Develop algorithm to implement variable steering (directly affects vehicle guidance algorithm)
  How do we (or do we need to) know turn position and/or only straight-ahead (home) position?
  Implement left and right turns (desire small turns, not full-limit turns)
  Differential wheel turn or single-side wheel turn?
  2-wheel or 4-wheel turn?
  Develop performance specification and algorithm interface description
Document, and brief post on, the motor speed and steering control performance specifications and algorithm interfaces
M
Encoder
Output
Speed
Command
-
+
A
B

## Slide 17: Motor Controller
The logic part of the input voltage: 6 ~ 12V
Driven part of the input voltage Vs: 4.8 ~ 46V
The logical part of the work current Iss: 36mA
Drive part of the operating current Io: 2A
Maximum power dissipation: 25W (T = 75 degree Celsius)
Control signal input level:
High level: 2.3V = Vin = Vss
Low:-0.3V = Vin = 1.5V
Operating temperature: -25 degree Celsius ~ +130 degree Celsius
Drive Type: Dual high-power H-bridge driver
Module Size: 47 mm × 53mm
Module Weight: About 29g

## Slide 18: Team 2 – Line-Follower Sensor Subsystem
Review information and evaluate sensor for:
  Line contrast/color detection
  Minimum/maximum line width
  Interference rejection (color sensitivity)
  Signal characteristics sent to controller (electrical interface)
  Power
  Size
  Weight
  Mounting requirements & location
Develop and conduct tests to characterize sensor performance to define the line track-error output
  Left, right, center
  Minimum line contrast required
  Minimum line width
  Minimum line radius of curvature (may be dependent on vehicle speed and/or line width)
  Define electrical interface
If sensor is inadequate, identify potential candidate sensors, select one or two to purchase, and characterize performance
Develop algorithm to provide error signal to controller
  Left-of-line, right-of-line, centered on-line
  Develop performance specification & algorithm interface description
Document, and brief post on, the performance specification and description of algorithm interface

## Slide 19: Line Tracking Sensor
This sensor is for line tracking purposes.
It detects white and black color, and it outputs via TTL signal.
Specification
  Power supply: +5V
  Operating current: <10mA
  Operating temperature range: 0°C ~ + 50°C
  3-wire output interface
  Output: TTL(Black for LOW output, White for HIGH output)

## Slide 20: Team 3 –Obstacle Detection Subsystem
Review information and evaluate sensors (ultrasonic and IR) for:
  Detection distance
  Field of view (in degrees) to minimize false alarms from objects outside of vehicle path
  False detections
  Signal characteristics sent to controller (electrical interface)
  Power
  Size
  Weight
  Mounting requirements
Develop and conduct tests to characterize sensor performance
  Field of view
  Approximate minimum size of object for reliable detection
  Typical detection distance
  Sensitivity to objects outside of vehicle path
  Define electrical interface
If sensors are inadequate, identify potential candidate sensors, select one or two to purchase, and characterize performance
Investigate potential use of an integrated detection system using both sensors
  Potentially use both acoustic (ultrasonic) and IR distance sensor? Use only one of them? – select one
Develop obstacle detection algorithm
  Determine signal threshold level for obstacle detection/recognition to minimize false alarms
  Rejection of obstacles outside of vehicle path?
  Other features………
  Develop performance specification & algorithm interface description
Document, and brief post on, the performance specification and description of algorithm interface

## Slide 21: Ultrasonic Sensor
The URM37 V3.2 Ultrasonic Sensor uses an industrial level AVR processor as the main processing unit. It comes with a temperature sensor which is unique in its class. The sensor has unique three output modes (PWM, RS232 or TTL) which allows it easy to adapt to most devices and applications. The sensor provides one channel servo control output which can be used for sweep function. The URM V3.2 Rev2 has a jumper which allows user to select RS232 level output or TTL level output. Specifications:
Power: +5V
Current: <20mA
Working temperature: -10 ~ +70 C
Detecting range: 4cm-3m (3-5m is possible, but depending on situations)
Resolution: 1cm
Interface: PWM, RS232 or TTL (via Jumper)
Servo control: One servo control output
Operating Mode: Serial (PWM) passive control mode; Autonomous Mode; On/OFF Mode
Temperature sensor: 12 bits reading from serial port
Size: 22mm × 51 mm
Weight: 30g

## Slide 22: IR Distance Sensor
The Sharp distance sensors are a popular choice for many projects that require accurate distance measurements. This IR sensor is more economical than sonar rangefinders, yet it provides much better performance than other IR alternatives. Interfacing to most microcontrollers is straightforward: the single analog output can be connected to an analog-to-digital converter for taking distance measurements, or the output can be connected to a comparator for threshold detection. The detection range of this version is approximately 10 cm to 80 cm (4" to 32"); a plot of distance versus output voltage is shown below.
Specifications:
  operating voltage: 4.5 V to 5.5 V
  average current consumption: 30 mA (typical)
  distance measuring range: 10 cm to 80 cm (4" to 32")
  output type: analog voltage
  output voltage differential over distance range: 1.9 V (typical)
  response time: 38 ± 10 ms
  package size: 29.5×13.0×13.5 mm (1.16×0.5×0.53")
  weight: 3.5 g (0.12 oz)

## Slide 23: Team 4 – Controller Software Executive Program Subsystem
Integrate algorithms for:
  Motor speed and steering control
  Line-follower detection
  Obstacle detection (ultrasonic and/or distance sensor)
  Develop vehicle guidance algorithm using the specifications and interface descriptions developed by the other three teams
  Determine how/when to use sensor information
  Execute go-forward, go-left, go-right, stop, reverse? commands as required
Determine what to do when an obstacle is detected
  Stop, reverse?, etc.
Develop fail-safe watchdog to stop vehicle if something goes wrong or track line ends
  Ex: If a line detection (or a change in track-error signal) is not received for a certain period of time, then stop vehicle and indicate a fault
Develop user interface – control and indicators
  Go/stop command
  Line detection indication
  Obstacle detection indication
  Fault indication
  Other features?
Develop software architecture description
Document, and brief post on, the controller software executive program architecture

## Slide 24: Controller Board
This is the DFRduino Mega 2560 V2.0. It is fully compatible with Arduino Mega 2560 R2. This board features the ATmega8U2 programmed as a USB-to-serial converter and it has a resistor pulling the 8U2 HWB line to ground, making it easier to put into DFU.
Specifications
  Compatible with Arduino Mega 2560 R2
  Microcontroller: ATmega2560
  Operating Voltage: 5V
  Input Voltage (recommended): 7-12V
  Digital I/O Pins: 54 (of which 14 provide PWM output)
  Analog Input Pins: 16
  DC Current per I/O Pin: 40 mA
  DC Current for 3.3V Pin: 50 mA
  Flash Memory: 256 KB of which 8 KB used by bootloader
  SRAM: 8 KB
  EEPROM: 4 KB
  Clock Speed: 16 MHz

## Slide 25: System Engineering & Project Management – Executive Committee
Conduct monthly design reviews to:
  Evaluate progress
  Review subsystem definitions:
    Subsystem descriptions and algorithm descriptions and interfaces
  Discuss problem areas & develop solutions
  Review system performance requirements (operational concept)
  Refine product performance requirements (operational concept) as necessary to accommodate issues encountered during product development and integration
Evaluate subsystem performance specifications and algorithm interface descriptions and software architecture:
  Motor & Steering Control Subsystem
  Line-Follower Sensor Subsystem
  Obstacle Detection Subsystem (acoustic and/or distance sensor)
  Controller Software Executive Program Subsystem
Develop and conduct tests to prove product meets performance requirements
Note: this committee will comprise 1 member of the 4 teams to implement a Systems Engineering “Executive Committee”

## Slide 26: Project Work Breakdown Structure (WBS)
Motor & Steering Control Subsystem
Line-Follower Sensor Subsystem
Obstacle Detection Subsystem
Software Executive Program Subsystem
System Engineering & Project Mgmt.
autoAuto Autonomous
Vehicle Product
Understand motor controller and encoder
Perhaps characterize encoder output
Develop algorithm to proportionally control motor speed
Develop algorithm to implement variable steering
Develop motor speed and steering control performance specifications and algorithm interfaces
Characterize sensor performance to define the line track-error output
Develop algorithm to provide error signal to controller
  Develop performance specification & algorithm interface
Characterize acoustic sensor performance
Characterize and investigate use of IR distance sensor
Decide whether to use both sensors integrated or which single sensor to use
Develop obstacle detection algorithm
Develop performance specification & algorithm interface
  Develop software architecture
  Integrate algorithms
  Develop vehicle guidance algorithm
  Determine what to do when an obstacle is detected
  Develop fail-safe watchdog to stop vehicle if something goes wrong or track line ends
  Develop user interface
Conduct monthly reviews and evaluate progress and definitions of each subsystem
Discuss problem areas and develop solutions
Review product performance requirements (operational concept)
Revise product performance requirements (operational concept) as required
Evaluate subsystem performance specifications, algorithms interfaces, and architecture
Develop and conduct tests to prove product meets requirements